## Slide 1: No Financial Conflicts of Interest
Abiy B. Ambaye, MD
Clinical Professor
University of Vermont College of Medicine
Diagnostic Challenges in COVID-19
P2P and ANADACH

## Slide 2
Vermont

## Slide 3: Vermont (pop 620K)
Florida

## Slide 4: Number of Tests per 100K Population Worldwide

## Slide 5: SARS-COV-2 Targets for Testing
Notes: Nucleocapsid: The genome + the protein coat of the virus (capsid)

## Slide 6: Levels of SARS-CoV-2 RNA, Antigen, and Antibody (IgM, IgG) after infection
http://www.diazyme.com/covid-19-antibody-tests
??
Antigen Test

## Slide 7: FDA Emergency Use Authorization (EUA)
https://www.fda.gov/medical-devices/emergency-situations-medical-devices/emergency-use-authorizations#covid19ivd
FDA EUA (July 27. 2020)*
103 Molecular/PCR
33 Serology
2 Antigen
* Currently are no FDA-approved tests

## Slide 8: Molecular (RT-PCR) Test
Gold standard, more accurate and reliable
But it is:
  Complex and highly centralized test
  Expensive
    Difficult to access by low and middle income countries (LMICs)
  Does not meet current demand worldwide
    ~500 million tests needed in LMICs over the next year
Rapid Diagnostic Tests (RDTs) can fill this gap
Notes:   75% of which in decentralized settings (i.e. primary healthcare, community-level care, hospital triage)
  high-performing, affordable, rapid diagnostic testing is available to everyone

## Slide 9: Rapid Diagnostic Tests (RDTs)
Antigen Test
Antibody Test

## Slide 10: Rapid Diagnostic Tests (RDTs)
Advantages:
  Easy to perform, faster results (minutes)
  Decentralized and portable
  Cheaper
Disadvantages:
  Lower Sensitivity (increased false negative rate)
    Sensitivity: from <50% to >96%
  Comparable specificity to molecular tests

## Slide 11: Antigen RDTs
For detection of active infection (similar to molecular)
More likely to be affordable (Target price $1/test)
Should meet performance requirements:
  High specificity (>97) and sensitivity (>80%)
  Increase manufacturing capacity in HIC & LMIC
  Available in a decentralized setting after short training
  Easy sample collection* without cold storage requirement
    * preferably self-collection: saliva, or nasal swab
  Easy to use procedures and results interpreted visually
Notes: Products must meet Target product profiles (TPP): not set yet for Antigen RDTs

## Slide 13: US FDA granted EUA 2 Antigen RDTs many more on the WHO website

## Slide 14: BD (Becton Dickinson) Veritor System for RDT Antigen Detection of SARS-CoV-2
Notes: Approved for EUA on July 2. 2020

## Slide 15
Qualitative detection of nucleocapsid antigens
Nasal swabs - first 5 days of symptom onset
Positive results: use for management
  High specificity
Negative results:
  Only presumptive - does not rule out infection
  Not be used as the sole basis for management
  Re-test with molecular
    If still suspected (exposure history & clinical findings)
BD Veritor System for Antigen RDT
Notes: use of product:
  nasal swab specimen is directly placed in the extraction reagent tube, during which time virus particles present in the specimen are disrupted, exposing internal viral nucleoproteins
  After that, the specimen is added to the BD Veritor System test device
  SARS-CoV-2 antigens present in the specimen then bind to antibodies conjugated to detector particles in the test strip
  The antigen-conjugate complexes migrate across the test strip to the reaction area and are captured by a line of antibodies bound on the membrane
  Test results are read when the 15-minute assay development time is complete
SARS-CoV-2 (+) Control Swab:
  swab is coated with non-infectious recombinant SARS antigens
  The positive control is used to monitor for failures of test cassette reagents and reaction conditions
SARS-CoV-2 (–) Control Swab:
  swab is dried with buffer solution and preservative, in the same formulation as the positive control without the signal protein.

## Slide 16: Performance BD Veritor System Antigen vs. Molecular
226 nasal swabs from symptomatic patients (within 5 days of onset)
Antigen RDT compared to results of molecular (RT-PCR) test
  Sensitivity = 84%
  Specificity = 100%
Notes: CLINICAL PERFORMANCE:
226 direct nasal swabs prospectively collected and enrolled from individual symptomatic patients (within 5 days of onset) who were suspected of COVID-19
As with all antigen tests, performance has been demonstrated to decrease as days since symptom onset increases
Nasal swabs were collected following the dual nares method
Specimens were frozen within 30 minutes of collection and stored until tested
The performance of the BD Veritor System Assay was compared to results of a nasopharyngeal or oropharyngeal molecular (RT-PCR) test

## Slide 17: Performance of RDTs in high & low prevalence COVID-19 infection
Notes: as seen below, a test with high performance (95%sensitivity and 98% specificity), when applied to a low- prevalence setting, will result in roughly the same number of true positives and false positives (PPV: ~50%),
whereas when applied to a higher prevalence population would result in a much higher positive predictive value (PPV: 95%), with the majority of positive results associated with actual cases. Alternatively,

## Slide 18: Antigen RDT (High performance: sens 95% and specif 98%)
1000 people with COVID-19 symptoms in Addis Ababa
  If prevalence of COVID-19 in Addis Ababa is:
  2% (PPV= 49.2%) 30% (PPV= 95%)
  285 True positive
  14 false positive
  686 True negative
  15 false negative
  19 True positive
  20 false positive
  960 True negative
  1 false negative
Notes: Remember: performance decreases as time from symptoms increases (more than 5 days)

## Slide 20: Sofia SARS Antigen FIA
209 direct nasal swabs from symptomatic patients
The Antigen RDT compared to molecular (RT-PCR) test
  Sensitivity = 96.7%
  Specificity = 100%
Notes: qualitative detection of the nucleocapsid protein antigen from SARSCoV-2 in nasopharyngeal (NP) and nasal (NS) swab specimens directly or after the swabs have been added to viral transport media from individuals who are suspected of COVID-19 by their healthcare provider
First FDA authorized (EUA) antigen test
Detects fragments of proteins on or in the virus
Samples from the nasal cavity using swabs
Authorized for use in high/moderate complexity labs and point-of-care (POC) testing
Sensitivity = 96.7% (95% CI = 37.6-96.4)
Specificity = 100% (95% CI = 91.8-100)
CLINICAL PERFORMANCE:
209 direct nasal swabs was performed
sequentially enrolled from symptomatic patients suspected of COVID-19 at five (5) locations
tested fresh at a single central laboratory
All patients had either a NP swab (for RT-PCR testing) and nasal swab (for Sofia testing) or matched nasal swabs collected for RT-PCR and Sofia testing
The Sofia SARS Antigen FIA was compared to the a Reference Extracted RT-PCR assay

## Slide 21: ACT Accelerator Initiative

## Slide 22: Serology (Antibody Testing)
Response to different targets in the virus:
  Anti-Spike (S) protein
    More specific
    Used for viral entry into host cell
    Needed for protection (neutralizing)
  Anti-Nucleocapsid (N) Protein
    Less specific
    Highly immunogenic and abundant
    Most available tests detect this protein

## Slide 23: Levels of SARS-CoV-2 RNA, Antigen & Antibody after infection
http://www.diazyme.com/covid-19-antibody-tests
??

## Slide 24: Serology (Antibody Test)
Host/patient response to infection
At least 10 days after infection
Can not distinguish between active and previous infection
Currently: can't confirm immunity to reinfection
aka Immunity Passport
More accurately estimates prior:
Infection Rate
Case Fatality Rate Incidence
Prevalence
FDA EUA requires:
90% sensitivity
95% specificity

## Slide 25: Serology - Utility
Screening previous exposure – beneficial
  Public health planning – case fatality rate (COVID-19 resurgence)
  Returning to work (aka Immunity Passport)?
    Protective effect and durability not yet determined
Screening currently infected patients – not beneficial
  In low prevalence of infection (very low PPV)
  Recent FDA warning regarding fraudulent claims
  Convalescent Serum: treatment of severely ill patients?

## Slide 26
Thank You
“in a pandemic, no one is safe until everyone is safe”